## Slide 1: Pedestrian Navigation with ESP32-CAM
Real-time obstacle detection, mapping and alerts

## Slide 2: Problem & Motivation
Pedestrians face hazards (potholes, obstacles) while walking
Existing navigation apps don't warn of local obstacles in real-time
Low-cost camera + edge/phone detection can fill this gap

## Slide 3: Project Objectives
Real-time obstacle detection and location reporting
Browser-based dashboard with live camera feed & map
Low-cost hardware integration (ESP32-CAM)
Trainable custom models for pothole/crack detection

## Slide 4: System Architecture
ESP32-CAM streams video (optional)
Browser or Python (YOLOv8) performs detection
Flask + Socket.IO server stores and broadcasts obstacles
Leaflet.js map shows geo-tagged obstacles in real-time

## Slide 5: Detection & Models
Prototype: TensorFlow.js COCO-SSD in browser (fast)
Server/desktop: YOLOv8 (Ultralytics) for higher accuracy
Planned: Custom YOLOv8 trained for potholes/cracks
Deduplication, distance-based warnings, configurable thresholds

## Slide 6: Web Application Features
Split-screen map + live camera (WebRTC or ESP32 stream)
Real-time WebSocket updates and analytics dashboard
Live detection panel with distance & priority warnings
Permission diagnostic tool and mobile-friendly UI

## Slide 7: ESP32-CAM Hardware
AI-Thinker ESP32-CAM (OV2640) streaming at /stream
FTDI programmer for uploads, 5V power, optional SD card
Mounting options: dashboard, helmet, chest, handlebar
Power: power bank or car USB for field deployment

## Slide 8: Demo (How to run)
Start Flask server: python web_app/server.py
Open: http://localhost:5000 (or phone on same WiFi)
Start camera and allow permissions (use external browser)
Optional: run esp32_detector.py to process ESP32 stream

## Slide 9: Results & Improvements
Higher accuracy with 75% threshold and YOLOv8 on backend
Deduplication prevents repeated alerts (30s cooldown)
Distance warnings: critical <3m, warning <10m
Real-time markers appear on map with user reports

## Slide 10: Next Steps
Train and deploy custom pothole/crack model (YOLOv8)
Integrate ESP32-CAM as primary camera source
Improve tracking to persist obstacles across frames
User testing and dataset collection in target areas

## Slide 11: Contact & Acknowledgements
Your Name — Project Lead
Supervisor: Prof. [Name]
Repo: https://github.com/Mohammedrafiullah1928/FINAL_YEAR_PROJECT
Questions? demo@youremail.com